## Slide 1: STM32CubeIDE Setup + Check
Embedded System

## Slide 2: Download stm32 CubeIDE
Enter download link: https://www.st.com/en/development-tools/stm32cubeide.html

## Slide 3: Download stm32 CubeIDE
Go down page till ‘Get Software’ part and download according to your OS

## Slide 4: Download stm32 CubeIDE
Accept License Agreement

## Slide 5: Download stm32 CubeIDE
Enter name and email. Don’t check box and press download

## Slide 6: Download stm32 CubeIDE
Check email from STMicroelectronics
Press ‘Download now’ button
New tab will open, wait a bit(might take some time)
New tab will open ‘st.com’ page and start downloading automatically
If download doesn’t start or you have any problems, try checking cookies

## Slide 7: Setup stm32 CubeIDE
Go to ‘File’->’New’->’STM32 Project’
Type ‘stm32l476’(It’s the letter ‘l’ not 1) in the ‘Commercial Part Number’ area
Check the list at the bottom right. Click the line with ‘Board’ as ‘NUCLEO~’ then press ‘next’

## Slide 8: Setup stm32 CubeIDE
Enter project name and change ‘Targeted Project Type’ to ‘Empty’.
Press ‘Finish’

## Slide 9: Setup stm32 CubeIDE
Right click project folder->press ‘Properties’

## Slide 10: Setup stm32 CubeIDE
Open ‘C/C++ General’->’Paths and Symbols’
Press ‘Add’->In ‘Directory’ box paste both ‘Include’ folders from downloaded ‘chip_headers’ file.(Extra explanation at next slide)
Press ‘OK’->’Apply’->’Apply and Close’

## Slide 11: How to get folder path
Open the folder that contains ‘chip_headers’ file
Go to ‘chip_headers’->’CMSIS’->’Include’
Click on address bar. Copy text. Paste to ‘Directory’ from previous slide. Press ‘OK’
Go to ‘chip_headers’ ’->’CMSIS’->’Device’ ->’ST’->’STM32L4xx’->’Include’
Click on address bar. Copy text. Paste to ‘Directory’ from previous slide. Press ‘OK’

## Slide 12: Setup stm32 CubeIDE
Open src->main.c File
Delete existing code and copy code
Connect board to PC(Check if board lights up)
Build code(Hammer button)
Upload code to board(Play button)
Board green LED should blink

## Slide 13: Setup stm32 CubeIDE: Font change
To change font / text size go to ‘Window’-> ’Preferences’
Drop down ‘General’->’Appearance’->Click ‘Colors and Fonts’
Basic->Click ‘Text Font’->Press ‘Edit’ button.
Edit font / font size