## Slide 1: USART
Embedded System

## Slide 2: USART - Registers
Datasheet(page 17)
USART2 connected to APB1
Order:
  Setup GPIO for USART2 output and input
  Enable clock APB1 for USART2 use
  Configure the USART

## Slide 3: USART - Registers
Datasheet(page 92), MB(page 2)
PA2, PA3 used for USART2_TX and USART2_RX
PA2 and PA3 need to be set to AF7 mode

## Slide 4: USART - Registers
Reference manual(page 303, 304)
To set the GPIO, change the MODEn[1:0] to [1, 1] for alternate function mode

## Slide 5: USART - Registers
Reference manual(page 308, 309)
Change GPIOx mode when using alternate functions
AF7 = 0111
A2, A3 need to be changed for USART output and input

## Slide 6: USART - Registers
Reference manual(page 254, 255)
To enable USART2 clock, change bit 17 to ‘1’

## Slide 7: USART - Registers
Reference manual(page 1395)
Used to setup baud rate

## Slide 8: USART - Registers
Reference manual(page 1384)
Used to enable, transfer, receive from USART
  Bit 0 : Enable USART
  Bit 2 : Enable receive from USART
  Bit 3 : Enable transfer from USART

## Slide 9: USART - Registers
Reference manual(page 1399, 1402)
Used to check if USART can send output or take input
‘1’ means that the USART can send / output

## Slide 10: PuTTY – Install
URL: https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html
Press ‘Next’ to every step and ‘Install’

## Slide 11: PuTTY – Configure
Search and open ‘device manager’
Check ‘Ports’
Remember the number after ‘COM’ for STM~
The port is ‘COM3’ here

## Slide 12: PuTTY – Configure
Open PuTTY
Open ‘Terminal’
Check both ‘Implicit~’ options

## Slide 13: PuTTY – Configure
Go back to ‘Session’
Change ‘Connection type’ to ‘Serial’
Set ‘Serial line’ to ‘COMn’(n is the number found in the above step)
Set ‘Speed’ to ‘115200’
Save the settings by
  Write name to ‘Saved Sessions’
  Press ‘Save’
  Next time, when you open PuTTY double click the name to open it.

## Slide 14: PuTTY – Configure
When you opened a blank terminal will open
Click the terminal to make the name show up at the top

## Slide 15: USART - Output
GPIO_Init function needed.
Will print ‘I’ on the screen constantly

## Slide 16: USART - Output

## Slide 17: USART – Output functions
Change the code to readable functions

## Slide 18: USART – Output functions
Change the code to readable functions

## Slide 19: USART – Output functions
Makes main function more readable and shorter

## Slide 20: USART – Output string
Takes a string and prints it to the terminal

## Slide 21: USART – Input
Takes an input from the terminal and returns it

## Slide 22: USART – Input
After printing the string ‘USART2 Connected!’
Takes input from the terminal and sends it back right away

## Slide 23: USART – Input

## Slide 24: Use header file to save functions
Make a ‘st_basic.h’ and ‘st_basic.c’ file at the ‘src’ file
Write the following code to ‘st_basic.h’ file

## Slide 25: Use header file to save functions
Put all the functions into the ‘st_basic.c’ file
Make sure to add the ‘#include “st_basic.h”’ line.

## Slide 26: Use header file to save functions
Change the ‘main.c’ file “stm32l476xx.h” to “st_basic.h”
Build and run code to check if it works

## Slide 27: Task 1
Make the board output a string “The button is pressed” / “The button is not pressed” if the button is pressed / not pressed accordingly
Add delay to prevent rapid output.

## Slide 28: Task 2
Make the LED LD2 change according to the input terminal
If the y key is inputted on the terminal turn the LED on
Else if the n key is inputted on the terminal turn the LED off