## Slide 1: GPIO
Embedded System

## Slide 2: GPIO - Registers
Datasheet(page 17)
GPIO PORT connected to AHB2
Order:
  Enable GPIO in AHB2
  Setup GPIO mode(input, output)
  If output set GPIO state

## Slide 3: GPIO - Registers
Reference manual(page 251)
To enable GPIOx we need to change the GPIOxEN bit to 1

## Slide 4: GPIO - Registers
Reference manual(page 303, 304)
To set GPIO to output or input, change the MODEn[1:0] to [0, 0] for input, [0, 1] for output

## Slide 5: GPIO - Registers
Reference manual(page 307)
To set output to ‘1’ write BSn to ‘1’
To set output to ‘0’ write BRn to ‘1’

## Slide 6: GPIO - Registers
Reference manual(page 306)
To check input from GPIO, check IDn for input state(0 or 1)

## Slide 7: Output in Board
User manual(page 23)
MB(page 4)
From diagram, User LED LD2 connected PA5 Pin
Can be used to check output

## Slide 8: Input in Board
User manual(page 23)
MB(page 2)
From diagram, User button B1 is connected to PC13.
Can be used to check input
PC13 is high when the button is not pressed and low then the button is pressed.

## Slide 9: GPIO Output
Try to type code, build, and run.
Should make the LD2 green light blink.
Order:
  Enable GPIO Clock
  Set GPIO input / output
  Toggle output

## Slide 10: GPIO Input
Try to type code, build, and run.
Should make the LD2 green light light up when the button is pressed.
Order:
  Enable GPIO Clock
  Set GPIO input / output
  Print output as LED

## Slide 11: GPIO Input - Code

## Slide 12: GPIO function